# Kenwood TK-830 Link Radio Wiring

Connections: Rear 15 pin Accessory Connector:

Pin 7 - Switched Battery

Pin 15 - Earth / Ground

Pin 5 - Mic High

Pin 4 - Discriminator ( Raw receive Audio)  See below for filtered Audio!!

Pin 8 - PTT

Pin 6 - Speaker Audio (15Watt / 4ohm, Pair w/ Pin 12 for External Speaker)

Pin 9 & 12 - Jumper For Internal Speaker

Pin 10  Cut Black Wire from CN104 Pin 5 inside radio Connect to CN107 Pin 7 with 10k res in series.

Control Board Option Connector CN107 Pin 7 - COR & PL - Active High - Goes high while receiving - Make sure to protect with a 10K resistor

For COR & PL - Active Low Add 2n3904 transistor

### COR- CN107 Pin 7 Location // Filtered Audio CN106 Pin 7

### Audio Mod  for filtered Audio Out

Un-plug Cn103 & CN104 from Control board. Remove 8 screws holding  Control board.

Tip board up find r133 / 220k resistor and remove, replace with ,1uf cap and 10k res in series as shown below. Re-assemble radio board.

Now you have filtered  low level Audio on CN106 pin  7.

To get it out the 15 pin Acc Jack, Remove (Pop out of Holder) Pin 3 wire (White/Yellow Stripe wire) from CN104 move it over to CN106 pin 7.

Now you have filtered audio on pin 4 of 15 pin acc jack on rear of Radio.